## Slide 1: Synthesis and Optimization of Switching Nanoarrays
Muhammed Ceylan Morgul
Mustafa Altun, PhD
Istanbul
Technical
University

## Slide 2: Outline
Introduction
  Shannon, CMOS, Moore’s Law, Nano Scale Electronic
  Self-Assembly Fabrication
  Switching Nanoarrays
Implementation Methodologies and Size Formulations
  Two-terminal Switch Based: Diode and CMOS
  Four-terminal Switch Based
Optimization
Experimental Results
Future Work and Discussion
Conclusion

## Slide 3: Introduction
1938: Claude Shannon’s thesis “A symbolic analysis of relay and switching circuits”
Carole Cable, www.cartoonstock.com

## Slide 4: Introduction
1963: CMOS
1965: Moore’s Law
  In every twelve months, number of elements in an IC (Integrated circuit) would be duplicated.
Even Gordon Moore himself claimed in 2005 that the validity of Moore’s Law will be lost.
  transistor’s physical working limits

## Slide 5: Introduction
Self-Assambly fabrication
  Cheap
  Ordered/Regular shaped
  Ex: Nanoarrays
Nano Scaled Technologies
  Single-electron transistors, quantum circuits, nanowires…
  Molecular and DNA computing
  Bottom-Up vs Top-Bottom Fabrications
A Boy And His Atom: The World's Smallest Movie, IBM
“Solar cells made through oil-and-water 'self-assembly”, http://news.bbc.co.uk, 2010

## Slide 6: Introduction
Switching Nanoarray

## Slide 7: Implementation Methodologies
Diode Based Switched Nanoarray
XOR2 = x1⊕ x2
Array Size = (number of products in f ) x (“number of literals in f ”+ 1)

## Slide 8: Implementation Methodologies
CMOS Based Switched Nanoarray
XOR2 = x1⊕ x2
Array Size = (number of literals in f ) x
(“number of products in f ” + “number of products in f D”)

## Slide 9: Implementation Methodologies
Four Terminal Switched Nanoarray
XOR2 = x1⊕ x2
Array Size = (number of products in f ) x (number of products in f D)

## Slide 10: Optimization
Algorithm steps:
Determine Upper Bound and Lower Bound for the function
The Implementable Nanoarray Shapes’ List
  The list is sorted in terms of array size
Check the shapes in the list
  Starting from the beginning of the list
Declare Optimal Size
for Four Terminal Switched Nanoarray

## Slide 11: Optimization
Target Function: XOR3 = x1⊕ x2 ⊕ x3
It and its dual have 4 # of products
UB = 4x4 = 16, LB = 9 (from the table)
The List: 3x3, 3x4, 4x3 and 4x4
(Example)
Altun and Reidel, Logic Synthesis for Switching Lattices, 2012
Lower Bound Table

## Slide 12: Optimization
Target Function: XOR3 = x1⊕ x2 ⊕ x3
The list: 3x3, 3x4, 4x3, 4x4
Check the target function can be realized in 3x3 or not
3x3 is the optimal solution
(Example continue)
X1 | X2 | 1
X2 | 0 | 0
X1’ | 0 | 0
X1 | X2 | 1
0 | 0 | 1
0 | 1 | 0
X1 | X3 | X1’
X2’ | 1 | X2
X1’ | X3’ | X1

## Slide 13: Optimization
Subdesign Library
Particular product
# of literals conflict for designs
Improvements
X1 | X3
X2’ | 1
X1’ | X3’
X1’ | 0
X2 | 0
X1 | 0
X1 | 0
X1 | X2
1 | 0
(e.g. with 6 variable in 3x4)
Discarded since has product X1

## Slide 14: Experimental Results

## Slide 15: Experimental Results

## Slide 16: Future Work and Discussion
The Sub-design Improvement makes the algorithm roughly 400 times faster for XOR3 (in 3x4)
Algorithm is implementable for any function,
but needs improvements to be more usefull for complex functions

## Slide 17: Conclusion
Investigations of Nanoarray Types
  Two and Four Terminal Switch Based
Size Formulation for Function Realization
  Diode and CMOS are optimum, Four-Terminal is not
Optimization for Four-Terminal
Comparison of Array Sizes of Nanoarray Types
  Using some Benchmark Functions

## Slide 18: Thank You All
The Scientific and Technological Council of Turkey,
Career Program
#113E760.
Emerging
Circuits and Computation Group
Istanbul
Technical
University