## Slide 1: Circuit Design and Optimization of Nano-Crossbar Arrays
12th Nanoscience and Nanotechnology Conference (NanoTR-12)
June 4th, 2016
Mustafa Altun, PhD
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Project Details
Gathers globally leading research groups working on nanoelectronics and EDA
Targets variety of emerging technologies including nanowire/nanotube crossbar arrays, magnetic switch-based structures, and crossbar memories
Contributes to the construction of emerging computers beyond CMOS by proposing nano-crossbar based computer architectures.
Budget: 724500 EURO

## Slide 3: Project Details

## Slide 4: Outline
Nano-crossbar arrays
Modeling nano-crossbar arrays and logic synthesis
  Diode based
  FET based
  Four-terminal switch based
Defect tolerance
R-C modelling
Performance optimization

## Slide 5: Motivation
1963: CMOS
1965: Moore’s Law
  Transistor count doubles every year.
1975: Moore’s Law updated
  Transistor count doubles every two years.
2015: Gordon Moore: «I see Moore’s law dying here in the next decade or so»
2015: Intel confirming the slowdown in pace of advancement, from two to two and a half years.
  Uncertainty, probabilistic phenomena
  Fabrication challenges
New technologies emerge: nano-crossbar arrays

## Slide 6: Emerging Transistors
Nanowire transistor
Single electron transistor
Direct and safe replacement of CMOS transistors
Some advantages over CMOS
Interconnection problems
Lack of integration
Carbon nanotube transistor
Spin based transistor
Quantum well transistor

## Slide 7: Nano-crossbar Arrays
Regular arrays
  Regularity; ease of design.
Nanotechnology
  Self-assembled systems.
Self-assembled nanowires
Self-assembled circuit with 64,000 elements in three minutes

## Slide 8: Why Self-assembly?
Directed assembly
  Advantages
    Results in a functional construct from a print/layout
  Disadvantages
    Costly in nanoscale
    Time consuming
Self assembly
  Advantages
    Fast and efficient in nanoscale
    Results in condensed structures
  Disadvantages
    Not results in a functional construct

## Slide 9: Modelling Nano-Crossbar Arrays
Nano array and 3 different crosspoint models

## Slide 10: Diode-based Model

## Slide 11: Diode-based Model
Example:
Implement the Boolean function f = A+B with diode based nanoarrays.
Diode-resistor logic

## Slide 12: Diode-based Model
Example:
Implement the Boolean function f = A B with diode based nanoarrays.
Diode-resistor logic

## Slide 13: Diode-based Model
Example:
Implement the Boolean function f = A B + C D with diode based nanoarrays.

## Slide 14: FET-based Model
From Snider, G., et al., (2004). CMOS-like logic in defective, nanoscale crossbars. Nanotechnology.

## Slide 15: FET-based Model
Example:
Implement the Boolean function f = Aꞌ with FET based nanoarrays using CMOS-like logic.

## Slide 16: FET-based Model
Example:
Implement the Boolean function f = (A B + C D)ꞌ with FET based nanoarrays using CMOS-like logic.

## Slide 17: Two-terminal vs. Four-terminal
Shannon’s work: A Symbolic Analysis of Relay and Switching Circuits(1938)

## Slide 18: Two-terminal vs. Four-terminal

## Slide 19: Two-terminal vs. Four-terminal
What are the Boolean functions implemented in (a) ad (b)?

## Slide 20: A Lattice of Four-terminal Switches
3 × 3 2D switching network and its lattice form

## Slide 21: Four-terminal Switch-based Model
Switches are controlled by Boolean literals.
fL evaluates to 1 iff there exists a top-to-bottom path.
gL evaluates to 1 iff there exists a left-to-right path.

## Slide 22: Logic Synthesis Problem
How can we implement a given target Boolean function fT with a lattice of four-terminal switches?
Example: fT = x1x2x3+x1x4

## Slide 23: Logic Synthesis Problem
Example: fT = x1x2x3+x1x4+x1x5
9 TOP-TO-BOTTOM PATHS!

## Slide 24: Synthesis Method
Example: fT = x1x2x3+x1x4+x1x5
fTD = (x1+x2+x3)(x1+x4)(x1+x5)
fTD = x1 + x2x4x5 + x3x4x5
Start with fT and its dual.
Assign each product of fT to a column.
Assign each product of fT D to a row.
Compute an intersection set for each site.
Arbitrarily select a literal from an intersection set and assign it to the corresponding site.

## Slide 25: Synthesis Method

## Slide 26: Math Behind the Method – Theorem 1
Theorem 1 (Altun and Riedel, 2010): If fT and fTD are implemented as subsets of all top-to-bottom and left-to-right paths, respectively, then fL = fT and gL = fTD.

## Slide 27: Math Behind the Method – Theorem 1
Theorem 1 allows us to only consider column-paths. We do not need to enumerate all paths!

## Slide 28: Math Behind the Method – Theorem 2
Theorem 2 (Altun and Riedel, 2010): Consider a product Pi of fT in ISOP form. For any literal x of Pi there exists at least one product Pj of fTD such that Pi ∩ Pj = x.
Lemma (Fredman and Khachiyan, 1996): Consider products Pi and Pj of fT and fTD in ISOP forms, respectively. Pi ∩ Pj ≠ Ø

## Slide 29: Math Behind the Method – Theorem 2
Theorem 2 (Altun and Riedel, 2010): Consider a product Pi of fT in ISOP form. For any literal x of Pi there exists at least one product Pj of fTD such that Pi ∩ Pj = x.
Each column is for each product!

## Slide 30: Method’s Performance
Size of the lattice: m×n
The time complexity:
O(m2n2)
n and m are the number of products of the target function fT and its dual fTD, respectively.

## Slide 31: Experimental Results

## Slide 32: Nano-Crossbar Arrays and Defects
Nano array and 3 different logic families
Defects are the main headache in nano arrays
Objective: Designing a fast heuristic algorithm for logic mapping on defective crossbars of 3 different logic families

## Slide 33: Defects in Diode based Nano Arrays
Ideally
f = A B + C D
Each crosspoint is either closed (diode connected) or open.
What if a crosspoint is closed when it is supposed to be open?
What if a crosspoint is open when it is supposed to be closed?
With a defect
f = A B + B C D
With a defect
f = A + C D
How to tolerate defects?

## Slide 34: Defects in FET based Nano Arrays
Ideally
f = (A B + C D)ꞌ
With a defect
f = 0
How to tolerate defects?
Each crosspoint is either closed (MOS or shorted) or open.
What if a crosspoint is closed when it is supposed to be open?

## Slide 35: Defects in Four-terminal Switch based Nano Arrays
Each crosspoint is either closed or open depending on the applied literal.
What if a crosspoint is always closed when it is supposed to switch?
What if a crosspoint is always open when it is supposed to switch?
Ideally
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
0
1
With a defect
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
With a defect
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
How to tolerate defects?

## Slide 36: Proposed Algorithm
Algorithm Steps:
Sort function and crossbar matrix
Obtain reduced matrix
Start subarray search
Compare sets of double indices, if equal sets found in 20,000 trials there is a matching, otherwise not.
Key concepts:
Row and column permutations of matrix produce equivalent logic function.
Double index is (a, b) tuple which shows the number of same elements in a row and a column
Necessary and sufficent condition: If two matrices have the same set of double indices, then they are identical

## Slide 37: Experimental Results
For each benchmark function, 600 crossbars are generated. 600 is chosen due to stabilization of tolerance fluctuations.
It takes 0.02 seconds in average to check a valid mapping that satisfies an accuracy of 99% compared with an exhaustive search.

## Slide 38: R-C Modeling of Arrays

## Slide 39: Performance Optimization

## Slide 40: 1-bit Full Adder Example

## Slide 41: Future Works

## Slide 42
THANK YOU!
Web: http://www.ecc.itu.edu.tr/